## Slide 1: ELECTRONIC CIRCUITS

## Slide 2: INTRODUCTION TO OP AMPS
An Operational Amplifier, or op-amp for short, is fundamentally a voltage amplifying device designed to be used with external feedback components such as resistors and capacitors between its output and input terminals.
These feedback components determine the resulting function or “operation” of the amplifier and by virtue of the different feedback configurations whether resistive, capacitive or both, the amplifier can perform a variety of different operations, giving rise to its name of “Operational Amplifier”.

## Slide 3
An Operational Amplifier is basically a three-terminal device which consists of two high impedance inputs. One of the inputs is called the Inverting Input, marked with a negative or “minus” sign, ( – ).
The other input is called the Non-inverting Input, marked with a positive or “plus” sign ( + ).
A third terminal represents the operational amplifiers output port

## Slide 4
A differential amplifier is a type of electronic amplifier that amplifies the difference between two input voltages but suppresses any voltage common to the two inputs.
The input stage is a diff amp, followed by more stages of gain, and a Class-B push-pull emitter follower.
Because a diff amp is the first stage, it determines the input characteristics of the op amp.
In most op amps, the output is single-ended, as shown.
With positive and negative supplies, the single-ended output is designed to have a quiescent value of zero.
This way, zero input voltage ideally results in zero output voltage.

## Slide 5
Advantages of the Push-Pull amplifier are: Due to Class B operation, their collector efficiency is quite high.
They give more AC output power per device.
Distortion free output is obtained.

## Slide 6
Figure 16-2a is the schematic symbol of an op amp.
It has noninverting and inverting inputs and a single-ended output.
Ideally, this symbol means that the amplifier has infinite voltage gain, infinite input impedance, and zero output impedance.
The ideal op amp represents a perfect voltage amplifier and is often referred to as a voltage-controlled voltage source (VCVS).
We can visualize a VCVS as shown in Fig. 16-2b, where Rin is infinite and Rout is zero.

## Slide 9
Summary Table 16-1 summarizes the characteristics of an ideal op amp.
The ideal op amp has infinite voltage gain, infinite unity-gain frequency, infinite input impedance, and infinite CMRR.
It also has zero output resistance, zero bias current, and zero offsets.
This is what manufacturers would build if they could.
What they actually can build only approaches these ideal values.

## Slide 10
When no feedback path (or loop) is used, the voltage gain is maximum and is called the open-loop voltage gain, designated AVOL.
In Summary Table 16-1,notice that the AVOL of the LM741C is 100,000.
Although not infinite, this open loop voltage gain is very high.
For instance, an input as small as 10 V produces an output of 1 V.
Because the open-loop voltage gain is very high, we can use heavy negative feedback to improve the overall performance of a circuit.

## Slide 11
Op amps are devices that many times are used to function as amplifiers. A voltage is input into the op amp and as output, it produces the voltage amplified. An ideal op amp will produce mega-gain, practically, it will be able to produce infinite voltage gain.
The input impedance of an electrical network is the measure of the opposition to current (impedance), both static (resistance) and dynamic (reactance), into the load network that is external to the electrical source.
An ideal constant voltage power supply should have zero output impedance so that changes in the load such as higher load currents do not cause a voltage drop at the output. In addition, the low impedance helps in reducing the noise and interference.

## Slide 12
The input bias current parameter, IIB, is defined as the average of the currents into the two input terminals with the output at a specified level. It is expressed in units of amperes.
The input offset current (IOS) is equal to the difference between the input bias current at the non-inverting terminal (IB+) minus the input bias current at the inverting (IB- ) terminal of the amplifier. Offset current is typically an order of magnitude less than bias current.
The input offset voltage (Vos) is a parameter defining the differential DC voltage required between the inputs of an amplifier, especially an operational amplifier (op-amp), to make the output zero (for voltage amplifiers, 0 volts with respect to ground or between differential outputs, depending on the output type)

## Slide 13: 16-2 The 741 Op Amp
In 1965, Fairchild Semiconductor introduced the A709, the first widely used monolithic op amp.
Although successful, this first-generation op amp had many disadvantages.
These led to an improved op amp known as the A741.
Because it is inexpensive and easy to use, the A741 has been an enormous success.
Other 741 designs have appeared from various manufacturers.
For instance, ON Semiconductor produces the MC1741, Texas Instruments the LM741, and Analog Devices the AD741.

## Slide 14: An Industry Standard
The 741 has become an industry standard.
Incidentally, the 741 has different versions numbered 741, 741A, 741C,741E, and 741N.
These differ in their voltage gain, temperature range, noise level, and other characteristics.
The 741C (the C stands for “commercial grade”) is the least expensive and most widely used.
It has an open-loop voltage gain of 100,000, an input impedance of 2 MV, and an output impedance of 75 V.

## Slide 15: Three popular package styles and their respective pinouts

## Slide 16: The Input Diff Amp

## Slide 17
The input stage is a diff amp (Q1 and Q2).
In the 741, Q14 is a current source that replaces the tail resistor.
R2, Q13, and Q14 are a current mirror that produces the tail current for Q1 and Q2.
Instead of using an ordinary resistor as the collector resistor of the diff amp, the 741 uses an active-load resistor.
This active-load Q4 acts like a current source with an extremely high impedance.
Because of this, the voltage gain of the diff amp is much higher than with a passive-load resistor.

## Slide 18: The Input Diff Amp

## Slide 19
The amplified signal from the diff amp drives the base of Q5, an emitter follower.
This stage steps up the impedance level to avoid loading down the diff amp.
The signal out of Q5 goes to Q6.
Diodes Q7 and Q8 are part of the biasing for the final stage.
Q11 is an active-load resistor for Q6.
Therefore, Q6 and Q11 are like a CE driver stage with a very high voltage gain.

## Slide 20: The Input Diff Amp

## Slide 21: The Final Stage
The amplified signal out of the CE driver stage (Q6) goes to the final stage, which is a Class-B push-pull emitter follower (Q9 and Q10).
Because of the split supply (equal positive VCC and negative VEE voltages), the quiescent output is ideally 0 V when the input voltage is zero.
Any deviation from 0 V is called the output error voltage.

## Slide 22
When v1 is greater than v2, the input voltage vin produces a positive output voltage vout.
When v2 is greater than v1, the input voltage vin produces a negative output voltage vout.
Ideally, vout can be as positive as +VCC and as negative as -VEE before clipping occurs.
The output swing is normally within 1 to 2 V of each supply voltage because of voltage drops inside the 741.

## Slide 23: The Input Diff Amp

## Slide 24: Active Loading
In Fig. 16-4, we have two examples of active loading (using transistors instead of resistors for loads).
First, there is the active-load Q4 on the input diff amp.
Second , there is the active-load Q11 in the CE driver stage.
Because current sources have high output impedances, active loads produce much higher voltage gain than is possible with resistors.
These active loads produce a typical voltage gain of 100,000 for the 741C.
Active loading is very popular in integrated circuits (ICs) because it is easier and less expensive to fabricate transistors on a chip than it is to fabricate resistors.

## Slide 25: The Input Diff Amp

## Slide 26: Frequency Compensation
In Fig. 16-4, Cc is a compensating capacitor.
Because of the Miller effect, this small capacitor (typically 30 pF) is multiplied by the voltage gain of Q5 and Q6 to get a much larger equivalent capacitance of:
where Av is the voltage gain of the Q5 and Q6 stages.
The resistance facing this Miller capacitance is the output impedance of the diff amp.
Therefore, we have a lag circuit.
This lag circuit produces a cutoff frequency of 10 Hz in a 741C.

## Slide 27
The open-loop gain of the op amp is down 3 dB at this cutoff frequency.
Then, AVOL decreases approximately 20 dB per decade until reaching the unity-gain frequency.
Figure 16-5 shows the ideal Bode plot of open-loop voltage gain versus frequency.
The 741C has an open-loop voltage gain of 100,000, equivalent to 100 dB.
Since the open-loop cutoff frequency is 10 Hz, the voltage gain breaks at 10 Hz and then rolls off at a rate of 20 dB per decade until it is 0 dB at 1 MHz.

## Slide 28
An op amp that is internally compensated, such as the 741C, has a first-order response.
Ie..a first-order response (20 dB per decade rolloff ), a second-order response (40 dB per decade rolloff ), a third-order response (60 dB per decade rolloff), and so on.

## Slide 29
Bias voltage is the amount of voltage that an electronic device needs in order to power on and function.
The input offset voltage is a parameter defining the differential DC voltage required between the inputs of an amplifier, especially an operational amplifier (op-amp), to make the output zero.
Common-mode means a signal that is equal=same on BOTH sides of the differential pair.
The op amp common-mode rejection ratio (CMRR) is the ratio of the common-mode gain to differential-mode gain. For example, if a differential input change of Y volts produces a change of 1 V at the output, and a common-mode change of X volts produces a similar change of 1 V, then the CMRR is X/Y.

## Slide 30: Bias and Off sets
A differential amplifier has input bias and offsets that produce an output error when there is no input signal.
In many applications, the output error is small enough to ignore.
But when the output error cannot be ignored , a designer can reduce it by using equal base resistors.
This eliminates the problem of bias current, but not the offset current or offset voltage.
This is why it is best to eliminate output error by using the nulling circuit given on the data sheet.
This recommended nulling circuit works with the internal circuitry to eliminate the output error and also to minimize thermal drift.
A slow change in output voltage caused by the effect of changing temperature on op-amp parameters.

## Slide 31
Figure 16-6 shows the nulling method suggested on the data sheet of a 741C.
The ac source driving the inverting input has a Thevenin resistance of RB.
To neutralize the effect of input bias current (80 nA) flowing through this source resistance, a discrete resistor of equal value is added to the noninverting input, as shown.
To eliminate the effect of an input offset current of 20 nA and an input offset voltage of 2 mV, the data sheet of a 741C recommends using a 10-kV potentiometer between pins 1 and 5.
By adjusting this potentiometer with no input signal, we can null or zero the output voltage.

## Slide 33: Common-Mode Rejection Ratio
For a 741C, CMRR is 90 dB at low frequencies.
Given equal signals, one a desired signal and the other a common-mode signal, the desired signal will be 90 dB larger at the output than the common-mode signal.
In ordinary numbers, this means that the desired signal will be approximately 30,000 times larger than the common-mode signal.
At higher frequencies, reactive effects degrade CMRR, as shown in Fig. 16-7a.

## Slide 34
Notice that CMRR is approximately 75 dB at 1 kHz, 56 dB at 10 kHz, and so on.

## Slide 35: Maximum Peak-to-Peak Output
The MPP value of an amplifier is the maximum peak-to-peak output that the amplifier can produce without clipping.
Since the quiescent output of an op amp is ideally zero, the ac output voltage can swing positively or negatively.
For load resistances that are much larger than Rout, the output voltage can swing almost to the supply voltages.
For instance, if VCC =+15 V and VEE =-15 V, the MPP value with a load resistance of 10 kV is ideally 30 V.

## Slide 36
Figure 16-7b shows MPP versus load resistance for a 741C with supply
voltages of +15 V and -15 V.
Notice that MPP is approximately 27 V for an RL of 10 kV.
This means that the output saturates positively at +13.5 V and negatively at -13.5 V.
When the load resistance decreases,
MPP decreases as shown.

## Slide 37: Short-Circuit Current
In some applications, an op amp may drive a load resistance of approximately zero.
In this case, you need to know the value of the short-circuit output current.
The data sheet of a 741C lists a short-circuit output current of 25 mA.
This is the maximum output current the op amp can produce.

## Slide 38: Frequency Response
Figure 16-7c shows the small-signal frequency response of a 741C.
In the mid band, the voltage gain is 100,000.
The 741C has a cutoff frequency fc of 10 Hz.
As indicated, the voltage gain is 70,700 (down 3 dB) at 10 Hz.
Above the cutoff frequency, the voltage gain decreases at a rate of 20 dB per decade (first-order response).
The unity-gain frequency is the frequency at which the voltage gain equals 1.
In Fig. 16-7c, funity is 1 MHz.

## Slide 40
Data sheets usually specify the value of funity because it represents the upper limit on the useful gain of an op amp.
For instance, the data sheet of a 741C lists an funity of 1 MHz.
This means that the 741C can amplify signals up to 1 MHz.
Beyond 1 MHz, the voltage gain is less than 1 and the 741C is useless.
If a designer needs a higher funity, better op amps are available.
For instance, the LM318 has an funity of 15 MHz, which means that it can produce usable voltage gain all the way to 15 MHz.

## Slide 41: Slew Rate
The compensating capacitor inside a 741C performs a very important function:
It prevents oscillations that would interfere with the desired signal.
But there is a disadvantage.
The compensating capacitor needs to be charged and discharged.
This creates a speed limit on how fast the output of the op amp can change.

## Slide 42
Here is the basic idea: Suppose the input voltage to an op amp is a positive voltage step, a sudden transition in voltage from one dc level to a higher dc level.
If the op amp were perfect, we would get the ideal response shown in Fig. 16-8a.
Instead, the output is the positive exponential waveform shown.
This occurs because the compensating capacitor must be charged before the output voltage can change to the higher level.
In Fig. 16-8a, the initial slope of the exponential waveform is called the slew rate, symbolized SR.
The definition of slew rate is:
where the Greek letter D (delta) stands for “the change in.”
In words, the equation says that slew rate equals the change in output voltage divided by the change in time.

## Slide 43
Figure 16-8b illustrates the meaning of slew rate.
The initial slope equals the vertical change divided by the horizontal change between two points on the early part of the exponential wave.
For instance, if the exponential wave increases 0.5 V during the first microsecond, as shown in Fig. 16-8c, the slew rate is:

## Slide 45
The slew rate represents the fastest response that an op amp can have.
For instance, the slew rate of a 741C is 0.5 V/s.
This means that the output of a 741C can change no faster than 0.5 V in a microsecond.
In other words, if a 741C is driven by a large step in input voltage, we do not get a sudden step in output voltage.
Instead, we get an exponential output wave.
The initial part of this output waveform will look like Fig. 16-8c.

## Slide 46
We can also get slew-rate limiting with a sinusoidal signal.
Here is how it occurs: In Fig. 16-9a, the op amp can produce the output sine wave shown only if the initial slope of the sine wave is less than the slew rate.
For instance, if the output sine wave has an initial slope of 0.1 V/s, a 741C can produce this sine wave with no trouble at all because its slew rate is 0.5 V/s.

## Slide 47
On the other hand, if the sine wave has an initial slope of 1 V/s, the output is smaller than it should be and it looks triangular instead of sinusoidal, as shown in Fig. 16-9b.

## Slide 48
With calculus, it is possible to derive this equation:
where SS is the initial slope of the sine wave, f is its frequency, and Vp is its peak value.
To avoid slew-rate distortion of a sine wave, SS has to be less than or equal to SR.
When the two are equal, we are at the limit, on the verge of slew-rate distortion.
In this case:
where fmax is the highest frequency that can be amplified without slew-rate distortion.

## Slide 49
The frequency fmax is sometimes called the power bandwidth or large-signal bandwidth of the op amp.
Figure 16-10 is a graph of Eq. (16-2) for three slew rates.
Since the bottom graph is for a slew rate of 0.5 V/s, it is useful with a 741C.
Since the top graph is for a slew rate of 50 V/s, it is useful with an LM318 (it has a minimum slew rate of 50 V/s).
For instance, suppose we are using a 741C.
To get an undistorted output peak voltage of 8 V, the frequency can be no higher than 10 kHz

## Slide 51
Example 16-1
How much inverting input voltage does it take to drive the 741C of Fig. 16-11a into negative saturation?

## Slide 52
Example 16-2
What is the common-mode rejection ratio of a 741C when the input frequency is 100 kHz?
SOLUTION
In Fig. 16-7a, we can read a CMRR of
approximately 40 dB at 100 kHz.
This is equivalent to 100, which
means that the desired signal receives
100 times more amplification than a
common-mode signal when the input
frequency is 100 kHz.

## Slide 53
Example 16-3
What is the open-loop voltage gain of a 741C when the input frequency is 1 kHz? 10 kHz? 100 kHz?
SOLUTION In Fig. 16-7c, the voltage gain is 1000 for 1 kHz, 100 for 10 kHz,and 10 for 100 kHz. As you can see, the voltage gain decreases by a factor of 10 each time the frequency increases by a factor of 10.

## Slide 54
Example 16-4
The input voltage to an op amp is a large voltage step. The output is an exponential waveform that changes to 0.25 V in 0.1 s. What is the slew rate of the op amp?
SOLUTION With Eq. (16-1):

## Slide 55
Example 16-5
The LF411A has a slew rate of 15 V/s. What is the power bandwidth for a peak output voltage of 10 V?
SOLUTION With Eq. (16-2):

## Slide 56
Example 16-6
What is the power bandwidth for each of the following?
              SR = 0.5 V/s and Vp = 8 V
              SR = 5 V/s and Vp = 8 V
              SR = 50 V/s and Vp = 8 V
SOLUTION With Fig. 16-10, read each power bandwidth to get these approximate
answers: 10 kHz, 100 kHz, and 1 MHz.