## Slide 1: UNIT 5

## Slide 2
Monolithic op amps are inexpensive, versatile, and reliable.
They can be used not only for linear circuits like voltage amplifiers, current sources, and active filters, but also for nonlinear circuits such as comparators, wave shapers, and active-diode circuits.
The output of a nonlinear op-amp circuit usually has a different shape from the input signal because the op amp saturates during part of the input cycle.
Because of this, we have to analyze two different modes of operation to see what happens during an entire cycle.

## Slide 3: 20-1 Comparators with Zero Reference
Often we want to compare one voltage with another to see which is larger.
In this situation, a comparator may be the perfect solution.
A comparator is similar to an op amp because it has two input voltages (noninverting and inverting) and one output voltage.
It differs from a linear op-amp circuit because it has a two-state output, either a low or a high voltage.
Because of this, comparators are often used to interface with analog and digital circuits.

## Slide 4: Basic Idea
The simplest way to build a comparator is to connect an op amp without feedback resistors, as shown in Fig. 20-1a.
Because of the high open-loop voltage gain, a positive input voltage produces positive saturation, and a negative input voltage produces negative saturation.

## Slide 5
The comparator of Fig. 20-1a is called a zero-crossing detector because the output voltage ideally switches from low to high or vice versa whenever the input voltage crosses zero.
Figure 20-1b shows the input-output response of a zero-crossing detector.
The minimum input voltage that produces saturation is:

## Slide 6
If Vsat = 14 V, the output swing of the comparator is from approximately -14 to +14 V.
If the open-loop voltage gain is 100,000, the input voltage needed to produce saturation is:

## Slide 7: Lissajous Pattern
A Lissajous pattern appears on an oscilloscope when harmonically related signals are applied to the horizontal and vertical inputs.
One convenient way to display the input/output response of any circuit is with a Lissajous pattern in which the two harmonically related signals are the input and output voltages of the circuit.

## Slide 8
For instance, Fig. 20-1c shows the input/output response for a 741C with supplies of ± 15 V.
Channel 1 (the vertical axis) has a sensitivity of 5 V/Div.
As we can see, the output voltage is either -14 or +14 V, depending on whether the Comparator is in negative or positive saturation.
Channel 2 (the horizontal axis) has a sensitivity of 10 mV/ Div.
In Fig. 20-1c, the transition appears to be vertical.
This means that the slightest positive input voltage produces positive saturation, and the slightest negative input produces negative saturation.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 9: Inverting Comparator
Sometimes, we may prefer to use an inverting comparator like Fig. 20-2a.
The noninverting input is grounded.
The input signal drives the inverting input of the comparator.
In this case, a slightly positive input voltage produces a maximum negative output, as shown in Fig. 20-2b.
On the other hand, a slightly negative input voltage produces a maximum positive output.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 10: Diode Clamps
The use of diode clamps is to protect sensitive circuits.
Figure 20-2a is a practical example.
Here we see two diode clamps protecting the comparator against excessively large input voltages.
For instance, the LM311 is an IC comparator with an absolute maximum input rating of ± 15 V.
If the input voltage exceeds these limits, the LM311 will be destroyed.
With some comparators, the maximum input voltage rating may be as little as ± 5 V, whereas with others it may be more than ± 30 V.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 11
In any case, we can protect a comparator against destructively large input voltages by using the diode clamps shown in Fig. 20-2a.
These diodes have no effect on the operation of the circuit as long as the magnitude of the input voltage is less than 0.7 V.
When the magnitude of the input voltage is greater than 0.7 V, one of the diodes will turn on and clamp the magnitude of the inverting input voltage to approximately 0.7 V.
When using one of these comparators, we have to add an external resistor in series with the input terminal.
This series resistor will limit the internal diode currents to a safe level.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 12: Converting Sine Waves to Square Waves
The trip point (also called the threshold or reference) of a comparator is the input voltage that causes the output voltage to switch states (from low to high or from high to low).
In the noninverting and inverting comparators discussed earlier, the trip point is zero because this is the value of input voltage where the output switches states.
Since a zero-crossing detector has a two-state output, any periodic input signal that crosses zero threshold will produce a rectangular output waveform.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 13
For instance, if a sine wave is the input to a noninverting comparator with a threshold of 0 V, the output will be the square wave shown in Fig. 20-3a.
As we can see, the output of a zero-crossing detector switches states each time the input voltage crosses the zero threshold.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 14
Figure 20-3b shows the input sine wave and the output square wave for an inverting comparator with a threshold of 0 V. With this zero-crossing detector, the output square wave is 180° out of phase with the input sine wave.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 15: Linear Region
Figure 20-4a shows a zero-crossing detector.
If this comparator had an infinite open-loop gain, the transition between negative and positive saturation would be vertical.
When the sensitivity of the 2 channel is changed to 200 V/Div, we can see that the transition is not vertical, as shown in Fig. 20-4b.
It takes approximately ± 100 V to get positive or negative saturation.
This is typical for a comparator.
The narrow input region between approximately -100 and +100 V is called the linear region of the comparator.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 16
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 17: Interfacing Analog and Digital Circuits
Comparators usually interface at their outputs with digital circuits such as CMOS,EMOS, or TTL (stands for transistor-transistor logic, a family of digital circuits).
Figure 20-5a shows how a zero-crossing detector can interface with an EMOS circuit.
Whenever the input voltage is greater than zero, the output of the comparator is high.
This turns on the power FET and produces a large load current.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 18
Figure 20-5b shows a zero-crossing detector interfacing with
a CMOS inverter.
The idea is basically the same.
A comparator input greater than zero produces a high input to the CMOS inverter.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 19
Most EMOS devices can handle input voltages greater than ± 15 V, and most CMOS devices can handle input voltages up to ±15 V.
Therefore, we can interface the output of a typical comparator without any level shifting or clamping.
TTL logic, on the other hand, operates with lower input voltages.
Because of this, interfacing a comparator with TTL requires a different approach.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 20: Clamping Diodes and Compensating Resistors
When a current-limiting resistor is used with clamping diodes, a compensating resistor of equal size may be used on the other input of the comparator, as shown in Fig. 20-6.
This is still a zero-crossing detector, except that it now has a compensating resistor to eliminate the effect of input bias current.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 21: Bounded Output
The output swing of a zero-crossing detector may be too large in some applications.
If so, we can bound the output by using back-to-back zener diodes, as shown in Fig. 20-7a.
In this circuit, the inverting comparator has a bounded output because one of the diodes will be conducting in the forward direction and the other will be operating in the breakdown region.
For instance, a 1N4731A has a zener voltage of 4.3 V. Therefore, the
voltage across the two diodes will be approximately ±5 V.
If the input voltage is a sine wave with a peak value of 25 mV, then the output voltage will be an inverted square wave with a peak voltage of 5 V.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 22
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 23
Figure 20-7b shows another example of a bounded output.
This time, the output diode will clip off the negative half-cycles of the output voltage.
Given an input sine wave with a peak of 25 mV, the output is bounded between
-0.7 and +15 V as shown.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 24
A third approach to bounding the output is to connect zener diodes across the output.
For instance, if we connect the back-to-back zener diodes of Fig. 20-7a across the output, the output will be bounded at ±5 V.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 25
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 26
This circuit compares two voltages of opposite polarity to
determine which is greater.
If the magnitude of v1 is greater than the magnitude of v2, the noninverting input is positive, the comparator output is positive, and the green LED is on.
On the other hand, if the magnitude of v1 is less than the magnitude of v2, the noninverting input is negative, the comparator output is negative, and the red LED is on.
If a 741C op amp is used, the LEDs at the output do not need current-limiting resistors because the maximum output current will be approximately 25 mA.
D1 and D2 are input clamping diodes.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 27
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 28
To begin with, the output diode D1 clips off the negative
half-cycles.
Figure 20-9 also contains a signal called a strobe.
When the strobe is positive, Q1 saturates and pulls the output voltage down to approximately zero.
When the strobe is zero, the transistor is cut off and the comparator output can swing positively.
Therefore, the comparator output can swing from -0.7 to +15 V when the strobe is low.
When the strobe is high, the output is disabled. In this circuit, the strobe is a signal used to turn the output off at certain times or under certain conditions.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 29
This is one way to create a 60-Hz clock, a square-wave signal used as the basic timing mechanism for inexpensive digital clocks.
The transformer steps the line voltage down to 12 Vac.
The diode clamps D1 and D2 then bound the input to 0.7 V.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 30
The inverting comparator produces an output square wave
with a frequency of 60 Hz.
The output signal is called a clock because its frequency can be used to get seconds, minutes, and hours.
A digital circuit called a frequency divider can divide the 60 Hz by 60 to get a square wave with a period of 1 s.
Another divide-by-60 circuit can divide this signal to get a square wave with a period of 1 min.
A final divide-by-60 circuit produces a square wave with a period of 1 hr.
Using the three square waves (1 s, 1 min, 1 hr) with other digital circuits and seven-segment LED indicators, we can display the time of day numerically.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 31: 20-2 Comparators with Nonzero References
In some applications, a threshold voltage different from zero may be preferred.
By biasing either input, we can change the threshold voltage as needed.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 32: Moving the Trip Point
In Fig. 20-11a, a voltage divider produces the following reference voltage for the inverting input:
When vin is greater than vref, the differential input voltage is positive and the output voltage is high.
When vin is less than vref, the differential input voltage is negative and the output voltage is low.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 33
A bypass capacitor is typically used on the inverting input, as shown in Fig. 20-11a.
This reduces the amount of power-supply ripple and other noise appearing at the inverting input.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 34
To be effective, the cutoff frequency of this bypass circuit should be much lower than the ripple frequency of the power supply.
The cutoff frequency is given by:
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 35
Figure 20-11b shows the transfer characteristic
(input/output response).
The trip point is now equal to vref. When vin is greater than vref, the output of the comparator goes into positive saturation.
When vin is less than vref, the output goes into negative saturation.

## Slide 36
A comparator like this is sometimes called a limit detector
because a positive output indicates that the input voltage exceeds a specific limit.
With different values of R1 and R2, we can set the limit anywhere between 0 and VCC.
If a negative limit is preferred, connect -VEE to the voltage divider, as shown in Fig. 20-11c.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 37
Now a negative reference voltage is applied to the inverting input.
When vin is more positive than vref, the differential input voltage is positive and the output is high, as shown in Fig. 20-11d.
When vin is more negative than vref, the output is low.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 38: Single-Supply Comparator
A typical op amp like the 741C can run on a single positive supply by grounding the -VEE pin, as shown in Fig. 20-12a.
The output voltage has only one polarity, either a low or a high positive voltage.
For instance, with VCC equal to +15 V, the output swing is from approximately +1.5 V (low state) to around +13.5 V (high state).
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 39
When vin is greater than vref, the output is high, as shown in Fig. 20-12b.
When vin is less than vref, the output is low.
In either case, the output has a positive polarity.
For many digital applications, this kind of positive output is preferred.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 40: IC Comparators
An op amp like a 741C can be used as a comparator, but it has speed limitations because of its slew rate.
With a 741C, the output can change no faster than 0.5 V/ µs.
Because of this, a 741C takes more than 50 s to switch output states with supplies of ±15 V.
One solution to the slew-rate problem is to use a faster op amp like an LM318.
Since it has a slew rate of 70 V/s, it can switch from -Vsat to +Vsat in approximately 0.3 s.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 41
Another solution is to eliminate the compensating capacitor found in a typical op amp.
Since a comparator is always used as a nonlinear circuit, a compensating capacitor is unnecessary.
A manufacturer can delete the compensating capacitor and significantly increase the slew rate.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 42: Open-Collector Devices
Figure 20-13a is a simplified schematic diagram for an open-collector comparator.
Notice that it runs off a single positive supply.
The input stage is a diff amp (Q1 and Q2).
A current source Q6 supplies the tail current.
The diff amp drives an active-load Q4.
The output stage is a single transistor Q5 with an open collector.
This open collector allows the user to control the output swing of the comparator.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 43
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 44
A typical op amp has an output stage that can be described as an active-pullup stage because it contains two devices in a Class-B push-pull connection.
With the active pullup, the upper device turns on and pulls the output up to the high output state.
On the other hand, an open-collector output stage of Fig. 20-13a needs external components to be connected to it.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 45
For the output stage to work properly, the user has to connect the open collector to an external resistor and supply voltage, as shown in Fig. 20-13b.
The resistor is called a pullup resistor because it pulls the output voltage up to the supply voltage when Q5 is cut off. When Q5 is saturated, the output voltage is low.
Since the output stage is a transistor switch, the comparator produces a two-state output.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 46
Examples of IC comparators are the LM311, LM339, and NE529.
They all have an open-collector output stage, which means that you have to connect the output pin to a pullup resistor and a positive supply voltage.
Because of their high slew rates, these IC comparators can switch output states in a microsecond or less.
The LM339 is a quad comparator—four comparators in a single IC package.
It can run off a single supply or off dual supplies.
Because it is inexpensive and easy to use, the LM339 is a popular comparator for general-purpose applications.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 47: Driving TTL
The LM339 is an open-collector device.
Figure 20-14a shows how an LM339 can be connected to interface with TTL devices.
A positive supply of +15 V is used for the comparator, but the open collector of the LM339 is connected to a supply of 15 V through a pullup resistor of 1 kV.
Because of this, the output swings between 0 and 15 V, as shown in Fig. 20-14b.
This output signal is ideal for TTL devices because they are designed to work with supplies of 15 V.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 49
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 50
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 51
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 52
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 53
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 54
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 55: 20-3 Comparators with Hysteresis
If the input to a comparator contains a large amount of noise, the output will be erratic when vin is near the trip point.
One way to reduce the effect of noise is by using a comparator with positive feedback.
The positive feedback produces two separate trip points that prevent a noisy input from producing false transitions.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 56: Noise
Noise is any kind of unwanted signal that is not derived from or harmonically related to the input signal.
Electric motors, neon signs, power lines, car ignitions, lightning, and so on produce electromagnetic fields that can induce noise voltages into electronic circuits.
Power-supply ripple is also classified as noise since it is not related to the input signal.
By using regulated power supplies and shielding , we usually can reduce the ripple and induced noise to an acceptable level.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 57
Thermal noise, on the other hand, is caused by the random motion of free electrons inside a resistor (see Fig. 20-16a).
The energy for this electron motion comes from the thermal energy of the surrounding air.
The higher the ambient temperature, the more active the electrons.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 58
The motion of billions of free electrons inside a resistor is pure
chaos.
At some instants, more electrons move up than down, producing a small negative voltage across the resistor.
At other instants, more electrons move down than up, producing a positive voltage.
If this type of noise were amplified and viewed on an oscilloscope, it would resemble Fig. 20-16b.
Like any voltage, noise has an rms or effective value.
As an approximation, the highest noise peaks are about four times the rms value.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 59: Noise Triggering
The high open-loop gain of a comparator means that an input of only 100 V may be enough to switch the output from one state to another.
If the input contains noise with a peak of 100 V or more, the comparator will detect the zero crossings produced by the noise.
Figure 20-17 shows the output of a comparator with no input signal, except for noise.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 60
When the noise peaks are large enough, they produce unwanted changes in the comparator output.
For instance, the noise peaks at A, B, and C are producing unwanted transitions from low to high.
When an input signal is present , the noise is superimposed on the input signal and produces erratic triggering.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 61: Schmitt Trigger
The standard solution for a noisy input is to use a comparator like the one shown in Fig. 20-18a.
The input voltage is applied to the inverting input.
Because the feedback voltage at the noninverting input is aiding the input voltage, the feedback is positive.
A comparator using positive feedback like this is usually called a Schmitt trigger.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 62
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 63
When the comparator is positively saturated, a positive voltage is fed back to the noninverting input.
This positive feedback voltage holds the output in the high state.
Similarly, when the output voltage is negatively saturated, a negative voltage is fed back to the noninverting input, holding the output in the low state.
In either case, the positive feedback reinforces the existing output state.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 64
The feedback fraction is:
When the output is positively saturated, the reference voltage applied to the noninverting input is:
When the output is negatively saturated, the reference voltage is:
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 65
The output voltage will remain in a given state until the input
voltage exceeds the reference voltage for that state.
For instance, if the output is positively saturated, the reference voltage is +BVsat.
The input voltage must be increased to slightly more than +BVsat to switch the output voltage from positive to negative, as shown in Fig. 20-18b.
Once the output is in the negative state, it will remain there indefinitely until the input voltage becomes more negative than
-BVsat.
Then, the output switches from negative to positive (Fig. 20-18b).
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 66
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 67: Hysteresis
The unusual response of Fig. 20-18b has a useful property called hysteresis.
To understand this concept, put your finger on the upper end of the graph where it says +Vsat.
Assume that this is the current value of output voltage.
Move your finger to the right along the horizontal line.
Along this horizontal line, the input voltage is changing but the output voltage is still equal to +Vsat.
When you reach the upper-right corner, vin equals +BVsat.
When vin increases to slightly more than +BVsat, the output voltage goes into the transition region between the high and the low states.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 68
If you move your finger down along the vertical line, you will simulate the transition of the output voltage from high to low.
When your finger is on the lower horizontal line, the output voltage is negatively saturated and equal to -Vsat.
To switch back to the high output state, move your finger until it reaches the lower-left corner.
At this point, vin equals -BVsat.
When vin becomes slightly more negative than -BVsat, the output voltage goes into the transition from low to high.
If you move your finger up along the vertical line, you will simulate the switching of the output voltage from low to high.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 69
In Fig. 20-18b, the trip points are defined as the two input
voltages where the output voltage changes states.
The upper trip point (UTP) has the value:
and the lower trip point (LTP) has the value:
The difference between these trip points is defined as the hysteresis (also called the dead band ):
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 70
Positive feedback causes the hysteresis of Fig. 20-18b.
If there were no positive feedback, B would equal zero and the hysteresis would disappear because both trip points would equal zero.
Hysteresis is desirable in a Schmitt trigger because it prevents noise from causing false triggering.
If the peak-to-peak noise voltage is less than the hysteresis, the noise cannot produce false triggering.
For instance, if UTP = +1 V and LTP = -1 V, then H = 2 V.
In this case, the Schmitt trigger is immune to false triggering as long as the peak-to-peak noise voltage is less than 2 V.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 71: Noninverting Circuit
Figure 20-19a shows a noninverting Schmitt trigger.
The input/output response has a hysteresis loop, as shown in Fig. 20-19b.
Here is how the circuit works: If the output is positively saturated in Fig. 20-19a, the feedback voltage to the noninverting input is positive, which reinforces the positive saturation.
Similarly, if the output is negatively saturated, the feedback voltage to the noninverting input is negative, which reinforces the negative saturation.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 72
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 73
Assume that the output is negatively saturated.
The feedback voltage will hold the output in negative saturation until the input voltage becomes slightly more positive than UTP.
When this happens, the output switches from negative to positive saturation.
Once in positive saturation, the output stays there until the input voltage becomes slightly less than LTP.
Then, the output can change back to the negative state.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 74
The equations for the trip points of a noninverting Schmitt trigger are given by:
The ratio of R1 to R2 determines how much hysteresis the Schmitt trigger has.
A designer can create enough hysteresis to prevent unwanted noise triggers.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 75: Speed-Up Capacitor
Besides suppressing the effects of noise, positive feedback speeds up the switching of output states.
When the output voltage begins to change, this change is fed back to the noninverting input and amplified, forcing the output to change faster.
Sometimes a capacitor C2 is connected in parallel with R2, as shown in Fig. 20-20a.
Known as a speed-up capacitor, it helps to cancel the bypass circuit formed by the stray capacitance across R1.
This stray capacitance C1 has to be charged before the noninverting input voltage can change.
The speed-up capacitor supplies this charge.

## Slide 77
To neutralize the stray capacitance, the minimum speed-up capacitance must be at least:
As long as C2 is equal to or greater than the value given by Eq. (20-12), the output will switch states at maximum speed.
Since a designer often has to estimate the stray capacitance C1, he or she usually makes C2 at least two times larger than the value given by Eq. (20-12).
In typical circuits, C2 is from 10 to 100 pF.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 78
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 79
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 80: 20-4 Window Comparator
An ordinary comparator indicates when the input voltage exceeds a certain limit or threshold.
A window comparator (also called a double-ended limit detector) detects when the input voltage is between two limits called the window.
To create a window comparator, we will use two comparators with different thresholds.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 81: Low Output between Limits
Figure 20-22a shows a window comparator that can produce a low output voltage when the input voltage is between a lower and an upper limit.
The circuit has an LTP and a UTP.
The reference voltages can be derived from voltage dividers, zener diodes, or other circuits.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 82
Figure 20-22b shows the input/output response of the window comparator.
When vin is less than LTP or greater than UTP, the output is high.
When vin is between LTP and UTP, the output is low.
Here is the theory of operation: For this discussion, assume the following positive trip points: LTP = 3 V and UTP = 4 V.
When vin < 3 V, comparator A1 has a positive output and A2 has a negative output.
Diode D1 is on and D2 is off.
Therefore, the output voltage is high.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 83
Similarly, when vin>4 V, comparator A1 has a negative output and A2 has a positive output.
Diode D1 is off, D2 is on, and the output voltage is high.
When 3 V < vin < 4 V, A1 has a negative output, A2 has a negative output, D1 is off, D2 is off, and the output voltage is low.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 84: High Output between Limits
Figure 20-23a shows another window comparator.
The circuit uses an LM339, which is a quad comparator that needs external pullup resistors.
When used with a pullup supply of +5 V, the output can drive TTL circuits.
A +15-V pullup supply can be used when driving power MOSFET circuits.
Figure 20-23b shows the input/output response.
As we can see, the output voltage is high when the input voltage is between the two limits.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 86
For this discussion, we are assuming the same reference voltages as in the preceding example.
When the input voltage is less than 3 V, the lower comparator pulls the output down to zero.
When the input voltage is greater than 4 V, the upper comparator pulls the output down to zero.
When vin is between 3 and 4 V, the output transistor of each comparator is cut off, so the output is pulled up to +5 V.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 87: 20-5 The Integrator
An integrator is a circuit that performs a mathematical operation called integration.
The most popular application of an integrator is in producing a ramp of output voltage, which is a linearly increasing or decreasing voltage.
The integrator is sometimes called the Miller integrator, after the inventor.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 88: Basic Circuit
Figure 20-24a is an op-amp integrator.
As you can see, the feedback component is a capacitor instead of a resistor.
The usual input to an integrator is a rectangular pulse like the one shown in Fig. 20-24b.
The width of this pulse is equal to T.
When the pulse is low, vin = 0. When the pulse is high, vin = Vin.
Visualize this pulse applied to the left end of R.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 90
Because of the virtual ground on the inverting input, a high
input voltage produces an input current of:
All this input current goes into the capacitor.
As a result, the capacitor charges and its voltage increases with the polarity shown in Fig. 20-24a.
The virtual ground implies that the output voltage equals the voltage across the capacitor.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 91
For a positive input voltage, the output voltage will increase negatively, as shown in Fig. 20-24c.
Since a constant current is flowing into the capacitor, the charge Q increases linearly with time.
This means that the capacitor voltage increases linearly, which is equivalent to a negative ramp of output voltage, as shown in Fig. 20-24c.
At the end of the pulse period in Fig. 20-24b, the input voltage returns to zero and the capacitor charging stops.
Because the capacitor retains its charge, the output voltage remains constant at a negative voltage of -V.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 92
The magnitude of this voltage is given by:
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 93
A final point: Because of the Miller effect, we can split the feedback capacitor into two equivalent capacitances, as shown in Fig. 20-24d.
The closed loop time constant for the input bypass circuit is:
For the integrator to work properly, the closed-loop time constant should be much greater than the width of the input pulse (at least 10 times greater).
As a formula:
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 94: Eliminating Output Offset
The circuit of Fig. 20-24a needs a slight modification to make it practical.
Because a capacitor is open to dc signals, there is no negative feedback at zero frequency.
Without negative feedback, the circuit treats any input offset voltage as a valid input voltage.
The result is that the capacitor charges and the output goes into positive or negative saturation, where it stays indefinitely.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 95
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 96
Another way to suppress the effect of input offset voltage is to use a JFET switch, as shown in Fig. 20-25b.
The reset voltage on the gate of the JFET is either 0 V or -VCC, which is enough to cut off the JFET.
Therefore, we can set the JFET to a low resistance when the integrator is idle and to a high resistance when the integrator is active.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 97
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 98
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 99: 20-6 Waveform Conversion
With op amps we can convert sine waves to rectangular waves, rectangular waves to triangular waves, and so on.
This section is about some basic circuits that convert an input waveform to an output waveform of a different shape.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 100: Sine to Rectangular
Figure 20-27a shows a Schmitt trigger, and Fig. 20-27b is the graph of output voltage versus input voltage.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 101
When the input signal is periodic (repeating cycles), the Schmitt trigger produces a rectangular output, as shown.
This assumes that the input signal is large enough to pass through both trip points of Fig. 20-27c.
When the input voltage exceeds UTP on the upward swing of the positive half-cycle, the output voltage switches to –V sat.
One half-cycle later, the input voltage becomes more negative than LTP, and the output switches back to +Vsat.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 102
A Schmitt trigger always produces a rectangular output,
regardless of the shape of the input signal.
In other words, the input voltage does not have to be sinusoidal.
This rectangular wave has the same frequency as the input signal.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 103
As an example, Fig. 20-27d shows a Schmitt trigger with
trip points of approximately UTP = +0.1 V and LTP = - 0.1 V.
If the input voltage is repetitive and has a peak-to-peak value greater than 0.2 V, the output voltage is a rectangular wave with a peak-to-peak value of approximately 2Vsat.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 104: Rectangular to Triangular
In Fig. 20-28a, a rectangular wave is the input to an integrator.
Since the input voltage has a dc or average value of zero, the dc or average value of the output is also zero.
As shown in Fig. 20-28b, the ramp is decreasing during the positive half-cycle of input voltage and increasing during the negative half-cycle.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 105
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 106
Therefore, the output is a triangular wave with the same frequency as the input.
It can be shown that the triangular output waveform has a peak-to-peak value of:
where T is the period of the signal.
An equivalent expression in terms of frequency is:
where Vp is the peak input voltage and f is the input frequency.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 107: Triangle to Pulse
Figure 20-29a shows a circuit that converts a triangular input to a rectangular output.
By varying R2, we can change the width of the output pulses, which is equivalent to varying the duty cycle.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 108
In Fig. 20-29b, W represents the width of the pulse and T is the period.
The duty cycle D is the width of the pulse divided by the period.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 109
In some applications, we want to vary the duty cycle.
The adjustable limit detector of Fig. 20-29a is ideal for this purpose.
With this circuit, we can move the trip point from zero to a positive level.
When the triangular input voltage exceeds the trip point, the output is high, as shown in Fig. 20-29c.
Since vref is adjustable, we can vary the width of the output pulse, which is equivalent to changing the duty cycle.
With a circuit like this, we can vary the duty cycle from approximately 0 to 50 percent.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 110
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 111
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 112
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 113
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 114: 20-7 Waveform Generation
With positive feedback, we can build oscillators, circuits that generate or create an output signal with no external input signal.
This section discusses some op-amp circuits that can generate non sinusoidal signals.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 115: Relaxation Oscillator
In Fig. 20-32a, there is no input signal. Nevertheless, the circuit produces a rectangular output signal.
This output is a square wave that swings between -Vsat and +Vsat.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 116
Assume that the output of Fig. 20-32a is in positive saturation.
Because of feedback resistor R, the capacitor will charge exponentially toward -Vsat, as shown in Fig. 20-32b.
But the capacitor voltage never reaches +Vsat because the voltage crosses the UTP.
When this happens, the output square wave switches to -Vsat.
With the output now in negative saturation, the capacitor discharges, as
shown in Fig. 20-32b.
When the capacitor voltage crosses through zero, the capacitor starts charging negatively toward -Vsat.
When the capacitor voltage crosses the LTP, the output square wave switches back to +Vsat.
The cycle then repeats.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 117
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 118
Because of the continuous charging and discharging of the
capacitor, the output is a rectangular wave with a duty cycle of 50 percent.
By analyzing the exponential charge and discharge of the capacitor, we can derive this formula for the period of the rectangular output:
where B is the feedback fraction given by:
Figure 20-32a is called a relaxation oscillator, defined as a circuit that generates an output signal whose frequency depends on the charging of a capacitor.
If we increase the RC time constant, it takes longer for the capacitor voltage to reach the trip points.
Therefore, the frequency is lower.
By making R adjustable, we can get a 50 : 1 tuning range.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 119: Generating Triangular Waves
By cascading a relaxation oscillator and an integrator, we get a circuit that produces the triangular output shown in Fig. 20-33.
The rectangular wave out of the relaxation oscillator drives the integrator, which produces a triangular output waveform.
The rectangular wave swings between +Vsat and -Vsat.
You can calculate its period with Eq. (20-18).
The triangular wave has the same period and frequency.
You can calculate its peak-to-peak value with Eq. (20-16).
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 120
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 121
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 122
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 123
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 124
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 125: 20-10 The Differentiator
A differentiator is a circuit that performs a calculus operation called differentiation.
It produces an output voltage proportional to the instantaneous rate of change of the input voltage.
Common applications of a differentiator are to detect the leading and trailing edges of a rectangular pulse or to produce a rectangular output from a ramp input.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 126: RC Differentiator
An RC circuit like the one shown in Fig. 20-40a can be used to differentiate an input signal.
The typical input signal is a rectangular pulse, as shown in Fig. 20-40b.
The output of the circuit is a series of positive and negative spikes.
The positive spike occurs at the same instant as the leading edge of the input, and the negative spike occurs at the same instant as the trailing edge.
Spikes like these are useful signals because they indicate when the rectangular input signal starts and ends.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 127
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 128
To understand how the RC differentiator works, look at
Fig. 20-40c.
When the input voltage changes from 0 to 1V, the capacitor begins to charge exponentially, as shown.
After five time constants, the capacitor voltage is within 1 percent of the final voltage.
To satisfy Kirchhoff’s voltage law, the voltage across the resistor of Fig. 20-40a is:
Since vC is initially zero, the output voltage suddenly jumps from 0 to V and then decays exponentially, as shown in Fig. 20-40b.
By a similar argument, the trailing edge of a rectangular pulse produces a negative spike. Incidentally, each spike in Fig. 20-40b has a peak value of approximately V, the size of the voltage step.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 129
If an RC differentiator is to produce narrow spikes, the time constant should be at least 10 times smaller than the pulse width T:
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 130
If the pulse width is 1 ms, the RC time constant should be less than 0.1 ms. Figure 20-40d shows an RC differentiator with a time constant of 0.1 ms.
If you drive this circuit with any rectangular pulse that has T greater than 1 ms, the output is a series of sharp positive and negative voltage spikes.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 131: Op-Amp Differentiator
Figure 20-41a shows an op-amp differentiator.
Notice the similarity to the op amp integrator.
The difference is that the resistor and capacitor are interchanged.
Because of the virtual ground, the capacitor current passes through the feedback resistor, producing a voltage across this resistor.
The capacitor current is given by this fundamental relation:
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 132
The quantity dv/dt equals the slope of the input voltage.
One common application of the op-amp differentiator is to produce very narrow spikes, as shown in Fig. 20-41b.
The advantage of an op-amp differentiator over a simple RC differentiator is that the spikes are coming from a low impedance source, which makes driving typical load resistances easier.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 133: Practical Op-Amp Differentiator
The op-amp differentiator of Fig. 20-41a has a tendency to oscillate.
To avoid this, a practical op-amp differentiator usually includes some resistance in series with the capacitor, as shown in Fig. 20-42.
A typical value for this added resistance is between 0.01R and 0.1R.
With this resistor, the closed-loop voltage gain is between 10 and 100.
The effect is to limit the closed-loop voltage gain at higher frequencies, where the oscillation problem arises.
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT

## Slide 134
RAMYA.SRIKANTESWARA,DEPARTMENT OF CSE,NMIT