## Slide 1: Design of Synchronous and Asynchronous Sequential Circuits

## Slide 2
Design problem normally starts with a word description of input output relation and ends with a circuit
diagram having sequential and combinatorial logic elements.
The word description is first converted to a state transition diagram or Algorithmic State Machine (ASM) chart followed by preparation of state synthesis table.
For flip-flop based implementation, excitation tables are used to generate design equations through Karnaugh Map.
The final circuit diagram is developed from these design equations.
In Read Only Memory (ROM) based implementation, excitation tables are not required however; flip-flops are used as delay elements.

## Slide 3
In this chapter, we show how these techniques can be used in sequential circuit design.
There are two different approaches of state machine design called Moore model and Mealy model.
In Moore model circuit outputs, also called primary outputs are generated solely from secondary outputs or memory values.
In Mealy model circuit inputs, also known as primary inputs combine with memory elements to generate circuit output.

## Slide 4: MODEL SELECTION
There are two distinct models by which a synchronous sequential logic circuit can be designed.
In Moore model the output depends only on present state and not on input.
In Mealy model ,the output is derived from present state as well as input.
The option to include input in output generation logic gives certain advantage to Mealy model.
Usually it requires less number of states and thereby less hardware to solve any problem.
If we want output transitions to be synchronized while input can change any time Mealy model is not preferred.
In Moore model, the output remains stable over entire clock period and changes only when there occurs a state change at clock trigger based on input available at that time.

## Slide 5: DESIGN OF SYNCHRONOUS SEQUENTIAL CIRCUIT

## Slide 6: The Problem
Design a sequence detector that receives binary data stream at its input, X and signals when a combination 'O 11' arrives at the input by making its output, Y high which otherwise remains low.
Consider, data is coming from left, i.e. the first bit to be identified is I, second I and third O from the input sequence.

## Slide 7: State Transition Diagram: Moore Model

## Slide 8: State Transition Diagram: Mealy Model

## Slide 9: Conversion of Models

## Slide 10: State Assignment
a:B=O, A=O b:B=O, A=l c:B=l, A=O d:B=I, A=l

## Slide 11: State Synthesis Table- Moore Model

## Slide 12: Design equations for Moore model,

## Slide 13: Circuit diagram following Moore model

## Slide 15: Design equations for Mealy models

## Slide 16: Circuit diagram following Mealy model

## Slide 17: ROM based implementation of sequence detector: Moore model

## Slide 18: ROM based implementation of sequence detector: Mealy model

## Slide 19: ALGORITHMIC STATE MACHINE
Algorithmic State Machine (ASM) is a flow chart like representation (ASM Chart) of the algorithm a state machine performs.
For relatively more complex problem where number of inputs and states are higher the state diagram space becomes so crowded that it is difficult to read.
The other advantage of ASM chart is that, it handles implementation issues with greater ease offering better timing infom1ation.
In ASM chart, square boxes represents a state.
If a state generates an unconditional output (Moore model) it can be specified within the square box.

## Slide 20
A diamond shaped box represents decision to be taken and normally the variable or the condition that is tested is placed inside it with a question mark.
There are two exit paths of this decision box since the decision is binary in nature.
For Mealy model, oval shaped boxes are used to describe the output that depends on present state as well as the present input.
Circles are used to denote start, stop of the algorithm and also the connector point of an ASM chart when it becomes too large and needs to be drawn at more than one place.
Entry and exit of each ASM block is shown by arrow headed connecting link.

## Slide 22: Vending Machine Problem
The task is to design a synchronous logic control unit of a vending machine.
The machine can take only two types of coins of denomination 1 and 2 in any order.
It delivers only one product that is priced Rs. 3.
On receiving Rs. 3 the product is delivered by asserting an output D = I
which otherwise remains 0.
If it gets Rs. 4 then product is delivered by asserting X and also a coin return mechanism is activated by output Y = 1 to return a Re. 1 coin.

## Slide 25: ASM Chart

## Slide 26: State Assignment and State Synthesis Table

## Slide 27: Design Equations from Karnaugh map and Circuit Diagram

## Slide 30: STATE REDuCTION TECHNIQUE

## Slide 31: Row Elimination Method

## Slide 36: Implication Table Method

## Slide 37: Reduce state transition diagram (Moore Model) ofFig. 11. l 7a by (i) row elimination method and (ii) implication table method