## Slide 1: HDL( HARDWARE DESCRIPTION LANGUAGE)

## Slide 2: INTRODUCTION TO HDL
The advantage of course, is to be able to
(i) Describe a large complex design requiring hundreds of logic gates in a convenient manner, in a smaller space,
(ii) Use software test-bench to detect functional error, if any, and correct it (called simulation) and finally,
(iii) get hardware implementation details (called synthesis).
Hardware Description Language, more popular with its acronym HDL is an answer for that.
Currently, there are two widely used HDLs-Verilog and VHDL (Very high speed integrated circuit
Hardware Description Language).
Verilog is considered simpler of the two and is more popular.
However, both share lot of common features and it is not too difficult to switch from one to the other.

## Slide 3: VERILOG HDL
Verilog as a hardware description language has a small history.
Introduced in 1980, primarily as a simulation and verification tool by Gateway Design Automation, it was later acquired by Cadence Data Systems.
Put to public domain in 1990, it gained popularity and is now controlled by a group of companies and universities,called Open Verilog International.
The reader with an exposure to any programming language like C will find it relatively easier to learn Verilog or any HDL.

## Slide 4: Describing Input/Output
In any digital circuit, we find there are a set of inputs and a set of outputs.
Often termed as ports, the relationship between these input and outputs are explained within the digital circuit.
To design any circuit that has say, three inputs a, b, c and two outputs say, x, y as shown in Fig. 2.37 the corresponding Verilog code can be written as shown next.

## Slide 5
Note that, module and endmodule written in bold are keywords for Verilog.
A module describes a design entity with a name or identifier selected by user (here, testckt) followed by input output port list.
This entity if used by another then arguments (i.e. ports) are to be passed in the same order as it appears here.
The symbol '//' is used to put comments and improve readability for a human but not used by the machine, i.e. compiler.
The module body describes the logic within the black box which acts on the inputs a, b, c and generates output x,y.
Observe, where semicolon';' is used and where not to end a statement, e.g. endmodule in above code does not end with semicolon.

## Slide 6: Writing Module Body
There are three different models of writing module body in Verilog HDL.
Each one has its own advantage and suited for certain kind of design.
We start with structural model by example of two-input OR gate described in Fig. 2.4a.

## Slide 7
Verilog supports predefined gate level primitives such as and, or, not, nand, nor, xor, xnor etc.
The syntax followed above can be extended to other gates and for 4 input OR gate itis as given next,or (output, input 1, input 2, input 3, input 4)
For NOT gate, not (output, input)
Note that, Verilog can take up to 12 inputs for logic gates.
Comments when extends to next line is written within /* ..... */.
Identifiers in Verilog are case sensitive, begin with a letter or underscore and can be of any length.

## Slide 9: Example 2

## Slide 12: Preparation of Test Bench
We take up the example of simulating a simple OR gate (Fig. 2.4a) for which Verilog code is already described.
The test bench, creates an input in the form of a timing waveform and passes this to OR gate module through a function or procedural can (passing arguments in proper order).

## Slide 16: HDL IMPLEMENTATION MODELS
We have seen how structural gate level modeling easily maps a digital circuit and replicates graphical symbolic representation.
We have also seen how a simple test bench can be prepared to test a designed circuit.
There, we generated all possible combinations of input variables and passed it to a circuit to be tested by providing realistic gate delays.

## Slide 17: Dataflow Modeling
Gate level modeling, though very convenient to get started with an HDL, consumes more space in describing a circuit and is unsuitable for large, complex design.
Verilog provides a keyword assign and a set of operators to describe a circuit through its behavior or function.
Here, we do not explicitly need to define any gate structure using and, or etc. and it is not necessary to use intermediate variables through wire showing gate level interconnections.
Verilog compiler handles this while compiling such a model.
All assign statements are concurrent, i.e. order in which they appear do not matter and also continuous, i.e. any change in a variable in the right hand side will immediately effect left hand side output.

## Slide 20: Behavioral Modeling
In a behavioral model, statements are executed sequentially following algorithmic description.
It is ideally suited to describe a sequential logic circuit.
However, it is also possible to describe combinatorial circuits with this but may not be a preferred model in most of the occasions.
It always uses always keyword followed by a sensitivity list.
The procedural statements following always is executed only if any variable within sensitivity list changes its value.
Procedure assignment or output variables within always must be of register type, defined by reg which unlike wire is not continuously updated but only after a new value is assigned to it.
Note that, wire variables can only be read and not assigned to in any procedural block, also it cannot store any value and must be continuously driven by output or assign statement.

## Slide 21
We note that, Y = AB + CD, i.e.
Y = 1 if AB = 11 or if CD = 11, otherwise Y = 0.
We use if ... else if ... else construct to describe this circuit.
Here, the conditional expression after if, if true executes one set of instructions else executes a different set following else or none at all.

## Slide 24: HDL IMPLEMENTATION OF DATA PROCESSING CIRCUITS
We start with hardware design of multiplexers using Verilog code.
The data flow model provides a different use of keyword assign in the form of assign X = S ? A : B;

## Slide 25
The behavioral model can be used to describe the 2 to 1 multiplexers in following two different ways, one using if ... else statement and the other using case statement.
The case evaluates an expression or a variable that can have multiple values each one corresponding to one statement in the following block.
Depending on value of the expression, one of those statements get executed.
The behavioral model of 2 to 1 multiplexer in both is given below:

## Slide 26
Design a 4 to 1 multiplexer using conditional assign and case statements.
We have used nested condition for assign statement.
If A= 1, condition ( B ? . D2) is evaluated. Then if B = 1, Y =. D3.
Similarly, the other combinations of A and B are evaluated and Y is assigned a. value from D2 to DO.

## Slide 27
For case statement we Conctenated A and B by using operator {.. } and generated four possible combinations, For a particular value of AB, statement corresponding to one of them gets executed..

## Slide 30
The circuit described by the HDL compares two 4-bit numbers A and B and generates a 3 bit output Y.
It has also a 3 bit input C.
If A is less than B, output Y = 001 and does not depend on C
Similarly, if A is greater than B, Y = 010 irrespective of C.
But if these two conditions are not met i.e. .A = B then Y = C.
If we consider three bits of Y represent (starting from MSB) A= B, A> Band A < B respectively then, this circuit represents a 4-bit magnitude comparator where C represents comparator output of previous stage that is of lower significance.
If numbers of this stage are equal then the value at C that represents equal, greater, less than condition of previous stage numbers is reflected by Y.